## Slide 1: Exploring the impact of Demand-Response actions on thermal comfort and energy costs in the residential sector in Greece
Technoeconomics of Energy Systems laboratory (TEESlab),
Department of Industrial Management & Technology,
University of Piraeus (UNIPI)
Assoc. Professor Dr. Alexandros Flamos

## Slide 2
Decarbonization of the European building sector towards 2050…
100% RES System using Storage & Demand-Response technologies
System Change
Decentralized community projects & innovative business models
Diffusion of technological breakthroughs at the residential sector
Digitalization can make this transition more efficient & democratic
Smart-Grid paradigm
Potential also lies in energy efficiency & tackling energy poverty

## Slide 3
Towards the decarbonization of the Greek building sector…
Building sector has significant room for decarbonisation
Six out of ten buildings have been constructed before 1980
25-30% of the final energy is consumed at the residential sector
Need of immediate renovations
Improved demand-side management (DSM)
Demand-Side Management (DSM) modeling
Demand-Response actions

## Slide 4
Why a new model ?
Bottom-up structure
Linking to other models & easily re-used
Linking to economic development & technological breakthrough
Outputs at a high resolution (1 minute)
Modular structure
Practical load control strategies that will allow price-based DR signals
Seasonal variability to reflect the changing level of demand between winter & summer
DSM modeling
Occupant behavior & determination of end-use qualities

## Slide 5
Bottom-up structure
Linking to economic development & technological breakthrough
Outputs at a high resolution (1 minute)
Modular structure
Practical load control strategies that will allow price-based DR signals
Seasonal variability to reflect the changing level of demand between winter & summer
DSM modeling
Occupant behavior & determination of end-use qualities
Dynamic high-Resolution dEmand-sidE Management model (1/2)
Linking to other models & easily re-used

## Slide 6
object-oriented programming
equation-based system modeling
dynamic simulation environment
DYMOLA
Horizon 2020
Dynamic high-Resolution dEmand-sidE Management model (2/2)

## Slide 7
Overall architecture
Parameters for n buildings
Weather climate data
Inputs
HVAC control settings
Occupancy profiles
Activity profiles
Demand-Response
Wholesale Electricity Market
Irradiance module
External temperature module
n number of buildings
Control strategies
Thermal comfort
Occupancy
Appliances
Smart thermostat
Net building electrical demand
HVAC
Electricity Storage
PV installation
Building envelope
Σ
-
Aggregated results for n buildings
Outputs
Main model

## Slide 8
Novelty (1/2)
interdependence of decisions within modules
independence of decisions between modules
hierarchical dependence of modules on components embodying standards & design rules
main principles of component- & modular-based system modeling approach
Modular structure

## Slide 9
Novelty (2/2)
Incremental modeling:
sub-models in multiple levels
Control capabilities: managing the complexity of large systems
Realistic representations of dynamic systems
Fast development & simulations: computational efficiency
Wide range of applications on Europe’s energy transition towards 2050

## Slide 10
Application: Decarbonisation of the Greek building stock
Evaluate the performance of conventional & smart EEMs
energy savings
return of investment
assessing economic benefits of each measure at a disaggregated (i.e., households) level
providing utilities & other potential end-users with useful insights
Energy poverty

## Slide 11
Research Question
How can Demand-Flexibility be brought into the Greek residential sector without jeopardizing thermal comfort and energy services of the occupants?
Application: Decarbonisation of the Greek building stock
Towards the Smart-Grid paradigm

## Slide 12
Parameters for n buildings
Weather climate data
Inputs
HVAC control settings
Occupancy profiles
Activity profiles
Irradiance module
External temperature module
n number of buildings
Control strategies
Thermal comfort
Occupancy
Appliances
Smart thermostat
Net building electrical demand
HVAC
Σ
Aggregated results for n buildings
Outputs
Main model
Demand-Response
Wholesale Electricity Market
Application: Decarbonisation of the Greek building stock
Electricity Storage
PV installation
-
Building envelope

## Slide 13
Scenario Analysis
Single Family House
Pre 1980
Reference Floor Area: 162m2
Single Family House
Post 2010
Reference Floor Area: 255m2
Adolescent
(12-18 years old)
School-aged child
(6-11 years old)
Greek nuclear (conjugal) family: 2 working parents & 2 children
Simulation period: 1/1–31/12 2020
Business-As-Usual (“SC1”)
Application: Decarbonisation of the Greek building stock

## Slide 14
Application: Decarbonisation of the Greek building stock
Scenario Analysis
Enabling next-generation of smart energy services valorizing EE and flexibility at demand-side as energy resource (“SC2”)
Single Family House
Pre 1980
Reference Floor Area: 162m2
Single Family House
Post 2010
Reference Floor Area: 255m2
Adolescent
(12-18 years old)
School-aged child
(6-11 years old)
Greek nuclear (conjugal) family: 2 working parents & 2 children
Simulation period: 1/1–31/12 2020

## Slide 15
Investment in smart infrastructure that enables demand-flexibility…
…allowing occupants to comply with DR signals, while operational & comfort constraints are not violated
Application: Decarbonisation of the Greek building stock
Scenario Analysis
Adolescent
(12-18 years old)
School-aged child
(6-11 years old)
DR Signals
Energy Supplier

## Slide 16
Boundary Conditions
Single Family House
Pre 1980
Single Family House
Post 2010
Weather Data
Application: Decarbonisation of the Greek building stock
Climatic Zone B
city of Athens

## Slide 17
Building Typologies
TABULA
webtool
Application: Decarbonisation of the Greek building stock
Single Family House
Pre 1980
Single Family House
Post 2010
Climatic Zone B
city of Athens

## Slide 18
Application: Decarbonisation of the Greek building stock
 | Thermal state of the body as a whole |  | 
Category | PPD (%) | PMV | Explanation
I | <6 | -0.2 < PMV < +0.2 | High level of expectation
II | <10 | -0.5 < PMV < +0.5 | Normal level of expectation
III | <15 | -0.7 < PMV < +0.7 | Acceptable, moderate level of expectation
IV |  |  | 
(a) | <20 | -1 < PMV < +1 | Marginal level of expectation
(b) | >20 | PMV < -1 or PMV > +1 | Inacceptable level of expectation
Thermal Comfort
Applicability of the thermal comfort categories of the EN 15251 standard

## Slide 19
Application: Decarbonisation of the Greek building stock
E
D
Environment
Agent
Output
Reward
State
Algorithm
Best Action
“real-world” approach
3-variable vector
- System Marginal Price (SMP)
- demand forecast
- actual demand
Initialization according to 2015 historical data
Central planner
Wholesale market
Input
Optimal mix of DR signals
Reinforcement Learning (RL)
A central planner attempts to
maximize flexibility value by issuing DR signals
Demand-Response

## Slide 20
Application: Decarbonisation of the Greek building stock
DR Control Strategy

## Slide 21
Results
Application: Decarbonisation of the Greek building stock
Acceptable Ranges of Indoor Temperature Setpoints
Thermal comfort categories of the EN 15251 standard
PMV
Temperature (oC)
Chart: Example
 | -4.6893 | 2.963
 | -3.7534 | 3.8996

## Slide 22
Results
Application: Decarbonisation of the Greek building stock
Single Family House
Pre 1980
Single Family House
Post 2010
 | Temperature ranges (oC) |  |  |  | 
 |  | Period 1 (Ap-My) | Period 1 (Oc-No) | Period 2 | Period 3
I |  | 24.57-25.38 | 24.31-25.09 | 24.77-25.51 | 22.95-24.09
II |  | 24.05-25.81 | 23.72-25.68 | 24.22-26.12 | 22.81-24.64
III |  | 23.69-26.16 | 23.33-26.07 | 23.85-26.43 | 22.45-25.01
IV(a) |  | 21.09-28.08 | 22.74-26.66 | 23.30-26.98 | 21.90-25.56
Temperature ranges (oC) |  |  |  |  | 
 | Period 1 (Ap-My) | Period 1 (Oc-No) | Period 2 | Period 3 | 
I | 22.35-23.18 | 23.69-24.48 | 24.44-25.24 | 21.86-22.67 | 
II | 21.72-23.81 | 23.10-25.07 | 23.85-25.83 | 21.25-23.29 | 
III | 21.31-24.22 | 22.70-25.47 | 23.44-26.23 | 20.84-23.69 | 
IV(a) | 20.68-24.85 | 22.11-26.06 | 22.85-26.83 | 20.23-24.31 | 
Acceptable Ranges of Indoor Temperature Setpoints
(I). Period 1 (mild weather): April, May, October, and November,
(II). Period 2 (hot weather): June to September,
(III). Period 3 (cold weather): December to March

## Slide 23
Results
Application: Decarbonisation of the Greek building stock
Impact of Demand-Response Actions on Thermal Comfort and Energy Cost
Single Family House
Pre 1980
Energy Consumption
(SC1-SC2)
Appliances
HVAC system
Single Family House
Post 2010

## Slide 24
Results
Application: Decarbonisation of the Greek building stock
No losses due to energy shifting during dynamic DR signals
Single Family House
Pre 1980
No sacrifices of energy needs & services
Impact of Demand-Response Actions on Thermal Comfort and Energy Cost
Single Family House
Post 2010

## Slide 25
Results
Application: Decarbonisation of the Greek building stock
Single Family House
Pre 1980
Impact of Demand-Response Actions on Thermal Comfort and Energy Cost
Single Family House
Post 2010
Thermal comfort at acceptable levels
maximum discomfort of 20% according to the Fanger theory
– PMV value in [-1.1]

## Slide 26
Results
Application: Decarbonisation of the Greek building stock
Single Family House Pre 1980
Energy savings due to small automated temperature setpoint
adjustments during dynamic DR signals
900 kWh

## Slide 27
Application: Decarbonisation of the Greek building stock
Energy savings due to small automated temperature setpoint
adjustments during dynamic DR signals
Results
Single Family House Post 2010
250 kWh

## Slide 28
Energy Supplier
In Summary
The RL optimal policy suggests a 16% raise in the retailer’s margin (compared to a no DR regime)
~ €1 billion at a National scale
Opportunity for extra revenue from the promotion of the full electrification of heating/cooling in the residential sector
Application: Decarbonisation of the Greek building stock
Consumers
Single Family House
Pre 1980
Single Family House
Post 2010
Savings

## Slide 29
Application: Decarbonisation of the Greek building stock
Additional Energy Efficiency (EE) Scenarios
“Saving Energy at Home II”
Programme

## Slide 30
Application: Decarbonisation of the Greek building stock
Additional Energy Efficiency (EE) Scenarios
EE Measure 2
Exterior Walls:
Insulation for NZEB scenario
Roof: Insulation - Tilted reinforced concrete slab with ceramic tile
EE Measure 4
EE Measure 3
Floor: Insulation - Slab on grade/ unheated space

## Slide 31
Application: Decarbonisation of the Greek building stock
Small-scale PV installation (1 kWp)
under the current Net-Metering policy scheme
EE Scenario 7
EE Measure 6
Replace incandescent or halogen bulbs with LED bulbs
EE Measure 5
Windows: Double Pane windows - Low-energy synthetic frame with thermal break
Additional Energy Efficiency (EE) Scenarios

## Slide 32
Application: Decarbonisation of the Greek building stock
where:
A: Discount Rate
B: Estimated Measure Life in Years
C: Total Investment Cost
D: Total kWh of Saved Energy

## Slide 33
Application: Decarbonisation of the Greek building stock
Measure Cost Data
EE Measure 2
EE Measure 4
EE Measure 3
 | Pre 1980 | Post 2010
A | 3% * | 
B | 40 years * | 
C | 4,080 € * | 7,040 € *
D | 1,576.50 kWh ** | 211.02 kWh **
 | Pre 1980 | Post 2010
A | 3% * | 
B | 40 years * | 
C | 3,060 € * | 6,000 € *
D | 764.30 kWh ** | 169.06 kWh **
 | Pre 1980 | Post 2010
A | 3% * | 
B | 40 years * | 
C | 3,300 € * | 5,840 € *
D | 4,320.77 kWh ** | 320.79 kWh **
EE Measure 5
 | Pre 1980 | Post 2010
A | 3% * | 
B | 25 years * | 
C | 3,450 € * | 3,960 € *
D | 805.20 kWh ** | 323.68 kWh **

## Slide 34
Application: Decarbonisation of the Greek building stock
Measure Cost Data
EE Measure 6
EE Measure 7
 | Pre 1980 | Post 2010
A | 3% * | 
B | 3 years * | 
C | 20 € * | 
D | 1,288.23 kWh ** | 
 | Pre 1980 | Post 2010
A | 3% * | 
B | 20 years * | 
C | 1,000 € * | 
D | 2,143.37 kWh ** | 
* Indicative Measure Cost Data, as obtained from the scientific literature and technical reports
** Energy Savings as derived from the model

## Slide 35
Application: Decarbonisation of the Greek building stock
Relationship between LCSE - Energy Savings
Single Family House – Pre 1980
Chart: Levelized Cost of Saved Energy (€/kWh)
| 0.11 | 0.17 | 3.3000000000000002E-2 | 0.25 | 3.3639999999999998E-3 | 3.1359999999999999E-2
 | 1576.5 | 764.3 | 4320.77 | 805.2 | 1288.23 | 2143.37
Break-even
0.203

## Slide 36
Application: Decarbonisation of the Greek building stock
Relationship between LCSE - Energy Savings
Single Family House – Post 2010
Chart: Levelized Cost of Saved Energy (€/kWh)
| 0.79 | 0.71 | 3.3639999999999998E-3 | 3.1359999999999999E-2
 | 320.79 | 323.68 | 1288.23 | 2143.37
Break-even
0.203

## Slide 37
Application: Decarbonisation of the Greek building stock
Single Family House
Pre 1980
Constructed before the Greek Regulation for Thermal Insulation in Buildings
Conclusions
EEM 1
EEM 2
EEM 3
EEM 4
EEM 6
EEM 7
Attractive EEMs

## Slide 38
Application: Decarbonisation of the Greek building stock
Attractive EEMs
Single Family House
Post 2010
Constructed according to the Greek Energy Performance of Buildings Directive (KENAK)
Conclusions
EEM 1
EEM 6
EEM 7

## Slide 39
Conclusions
Increased demand-flexibility can be brought to the Greek building sector without:
I. Significant changes in the current market design,
II. Consumers sacrificing thermal comfort & energy services
“Game-changer” business models that capture new value on the supply side by coupling it to the demand side
Synergistic co-operation between the power supplier & consumers, could lead to significant cost reductions & energy savings
Application: Decarbonisation of the Greek building stock
Smart EEMs seem equally/more attractive than traditional measures for both cases

## Slide 40
inclusion of socioeconomic & demographic factors
customer profiles
particularities of energy poor households
selection of
tailor-made
EEMs
maximum
impact
Further Research…
Evaluate the performance of conventional & smart EEMs
energy savings
return of investment
Energy poverty

## Slide 41
structured policy framework to motivate people regulating energy consumption
financial benefits from obtaining energy saving practices
Incentives
Human behavior
Energy efficiency
Energy Currency
Computational Monetary Framework
Further Research…

## Slide 42
Incentives
Human behavior
Energy efficiency
Energy Currency
Sharing economy
Further Research
Peer-to-Peer” (P2P) energy trading
Further Research…

## Slide 43
Next Steps Forward…
Supporting efforts around Europe towards open modeling:
publicly available through existing channels
source code
open licenses
public transparency
scientific reproducibility
open source development
documentation
datasets

## Slide 44
A central planner attempts to maximize flexibility value by issuing DR signals
Evaluate what should be considered a realistic response under different DR signals
For a given flexibility level, quantify the monetary value when brought to market
Given the monetary value, quantify the total value of different technology combinations
Given the value for consumers, derive pathways for technology adoption
A
C
B
E
D
Business Models (BMs) to explore benefits of self-consumption & demand-flexibility in the power market

## Slide 45
Find more about us…
For more information…
Contact us by e-mail:
teeslab@unipi.gr
Visit our Website:
https://teeslab.unipi.gr/
Find us in LinkedIn:
www.linkedin.com/groups/12070918/
TEESlab, the energy modelling, strategy and policy analysis laboratory of University of Piraeus (UNIPI)

## Slide 46
Thank you !
Alexandros Flamos aflamos@unipi.gr